## Slide 1: Reconciling SCXML Statechart Representations and Event-B Lower Level Semantics
Karla Morris : Sandia National Laboratories, CA, USA
Colin Snook : University of Southampton, UK

## Slide 2: Outline
Motivation
Model Representations
  SCXML
  iUML-B
  Similarities & Differences in the Semantics
Extensions to SCXML
Prototype System Model
Future Work
Conclusions

## Slide 3: Motivation
Event-B provides verification by formal proof…
… but notation is restricted to simplify verification.
Engineers are used to a richer notation..
.. they may find the restrictions difficult to accept.
iUML-B State-machines help but still close to Event-B.
Can Harel style state-chart semantics be reconciled with iUML-B?
We investigate a translation from SCXML state-charts to iUML-B state-machines (and hence to Event-B).

## Slide 4: SCXML: State Chart eXtensible Markup Language
State Chart XML :
  State Machine Notation for Control Abstraction
XML notation
Harel Statecharts
Executable (via simulator tools)
Related to CCXML Call Control XML, event-based telephony

## Slide 5: SCXML
<?xml version="1.0"?>
<scxml xmlns="http://www.w3.org/2005/07/scxml"
version="1.0"
datamodel="ecmascript"
initial="off">
<!-- trivial 5 second microwave oven example -->
<datamodel>
<data id="cook_time" expr="5"/>
<data id="door_closed" expr="true"/>
<data id="timer" expr="0"/>
</datamodel>
<state id="off">
<!-- off state -->
<transition event="turn.on" target="on"/>
</state>
<state id="on">
<initial>
<transition target="idle"/>
</initial>
<!-- on/pause state -->
<transition event="turn.off" target="off"/>
<transition cond="timer &gt;= cook_time” target="off"/>
<state id="idle">
<!-- default immediate transition if door is shut -->
<transition cond="door_closed" target="cooking"/>
<transition event="door.close" target="cooking">
<assign location="door_closed" expr="true"/>
<!-- start cooking -->
</transition>
</state>
<state id="cooking">
<transition event="door.open" target="idle">
<assign location="door_closed" expr="false"/>
</transition>
<!-- a 'time' event is seen once a second -->
<transition event="time">
<assign location="timer" expr="timer + 1"/>
</transition>
</state>
</state>
</scxml>

## Slide 6: iUML-B Statemachines

## Slide 7: iUML-B Statemachines

## Slide 8: Similarities
Hierarchical nested state-charts
Transitions with
  Conditions / Guards
  Actions
States can have Entry and Exit Actions
  (use with care in iUML-B)

## Slide 9: Differences
Event-B has..
  Refinement
  Invariants
SCXML has..
  External Trigger events
    Hence transitions do not have a name/label
  Sequential actions
  Run to Completion – Big step/little step

## Slide 10: SCXML Extensions
XML tools allow new meta-model ‘namespaces’ to be introduced.
  Existing SCXML tools will ignore them
Needed in order to support:
  Refinement levels (new attribute <iumlb:refinement …>)
  Invariants (new element <iumlb:invariant …>)
  Guards (new element <iumlb:guard …>)

## Slide 11: SCXML Extension Attributes

## Slide 12: Example extended SCXML (extensions are captured in red)
<datamodel iumlb:refinement="2">
<data expr="false" id="Gate_In.Block" iumlb:type="BOOL"/>
</datamodel>
<!-- Other model details -->
<state id="BLOCKED">
<transition cond="[On_In.CardAccept==true]" target="UNBLOCKED">
<iumlb:guard name="gd1" predicate="On_In.CardAccept==true" refinement="2"/>
<assign expr="true" location="Gate_In.Block" iumlb:refinement="3"/>
</transition>
<onentry>
<assign expr="true" location="Gate_In.Block"/>
<assign expr="false" location="On_In.Reset"/>
</onentry>
<onexit>
<assign expr="false" location="Gate_In.Block"/>
</onexit>
<iumlb:invariant predicate="Gate_In.Block == TRUE" name="GateCondition"/>
</state>

## Slide 13: Initial translation supports..
Data models
Hierarchical nested statemachines
Parrallel Statemachines
‘When’ Transitions (label)
Transition parameters, guards and actions
Invariants
Initial and Final states
Refinement (superposition only)

## Slide 14: Diagram of SCXML

## Slide 15: Example – generated iUML-B

## Slide 16: Next steps
Try modelling the run to completion semantics
E.g. trigger events create a token,
  A new token can only be consumed when no transitions are enabled
Try enforcing transition run-to-completion sequences
Still omit sequencing of actions

## Slide 17: Enhance iUML-B to support triggers
iUML-B Statemachines will own a collection of triggers.
  Each trigger will generate an Event-B BOOL variable.
    (Note simplification of SCXML, which permits several triggers of a kind to be queued).
  Transitions may reference a trigger.
    The reference will generate a guard, <trigger variable> = TRUE
    And an action <trigger variable> := FALSE.
  Transitions may own a collection of ‘Raise’ actions that reference an internal trigger.
    This will generate an action <trigger variable> := TRUE.
  Transitions may be designated as external.
    An interface event will be generated to create a new trigger ( <trigger variable> := TRUE )
    when it has been consumed ( <trigger variable> = FALSE ) and
    No transitions are enabled. (run to completion)
A partial ‘run-to-completion’ semantics will be introduced by disabling all interface events while any external or internal transition is enabled.

## Slide 18: External Trigger Event
Old trigger has been consumed
Raise new trigger
No transitions enabled

## Slide 19: Triggered transition
The trigger guard
Raise an internal trigger
Consume the external trigger

## Slide 20: Conclusions
Strong motivation from engineers
Difficult to reconcile semantic differences
  Run-to-completion, Sequential execution
We adopt a compromise
  Support what we can
    Add extensions where necessary
  Otherwise, restrict SCXML

## Slide 21: Thank you
Questions?